## Slide 1: Interrupts
Week 6

## Slide 2: What is an interrupt?
Asynchronous
Break of execution
Performs a routine then returns
Exceptions
System Calls
Device Notifications

## Slide 3: Why are interrupts necessary?
They aren’t
Alternative approaches:
  Polling – slow, inefficient, blocking
  Proper concurrency – Transputer, XMOS
Are necessary on current architectures
No other way to create responsiveness to real time events
Not necessary for scheduling:
  Co-operative processing
But necessary for pre-emptive (software driven) scheduling

## Slide 4: So are interrupts a good thing?
No
They are the best hack solution to a bad situation

## Slide 5: x86: Real vs Protected mode interrupts
Real mode – Interrupt Vectors Table
Protected mode – Interrupt Descriptors Table
We are in protected mode

## Slide 6: x86 : Interrupt Descriptors Table
Configuration table
Same as GDT in setup steps (also has a pointer structure)
Each entry has 8 bytes
Offset : Pointer to handler method
Present : Whether the handler exists
DPL : Privilege level
S : Storage Segment
Type : 16/32 bit, Task, Interrupt or Trap
Selector : Code Segment Selector for handler method

## Slide 7: MIPS : Fixed handler address(es)
MIPS always jumps to same address for interrupts
Different modes (names?)
  0xB….. For one mode
  0x80000180
Can also enable separate IRQ handler address:
  0x80000200
How to configure the interrupt handler(s)?
  Bootloader needs to copy the code into the right place
  Or your OS can copy it in
  But remember the cached/uncached segments

## Slide 8: Devices, Timers and IRQ
IRQ = Interrupt ReQuest
Device = Anything attached to the I/O bus
Timer = Most common /important device, often more than 1
x86 Timer = Programmable Interval Timer (PIT)
  3 timers of which:
    1 main timer used for scheduling
    1 removed/deprecated
    1 for PC speaker (often not present in modern PCs)
      VM vs. emulator
Interrupts used to notify OS when a task has completed
Interrupt flooding is a serious problem

## Slide 9: IRQ go through PIC
PIC = Programmable Interrupt Controller
Buffers IRQs from devices
Prioritises IRQs from devices
Maps IRQ numbers to ISRs (Interrupt Service Routine)
Masks IRQ interrupts
  Global mask (in processor)
  Mask register in PIC

## Slide 10: PIT configuration
http://www.flingos.co.uk/docs/reference/Programmable-Interval-Timer/
Steps required:
  [Enter protected mode]
  Setup entries in IDT
  Tell processor about the IDT
  Configure PIC
  Unmask timer IRQ in PIC
  Enable maskable interrupts (global flag)
  Handle the interrupt

## Slide 11: Your turn…