## Slide 1: Week 1 & 2
x86 and MIPS Architectures

## Slide 2: Re-cap (1)
Registers = Temporary storage (for performing operations)
Stack = Temporary storage (e.g. return address, locals, arguments)
Heap = Large or long-term storage (e.g. for arrays)
Processor executes instructions: Operation + Data
Instructions executed in order: Instruction Pointer ([E]IP)
More registers: Control, Debug, Flags – Flags used for core features + conditional branches (jumps)
Other processor features:
  ALU
  FPU(?)
  EPU – Exception Processing Unit : Remember, Exception = Interrupt (and not always an error)
  MMU – Memory Management Unit : Remember, also controls access to I/O Ports
I/O Ports – For accessing devices

## Slide 3: Re-cap (2)
Boot sequence
Use pre-built bootloader
ROM (PCs: BIOS, MIPS: Das UBoot)
  Often writeable these days.
  Variable size
  Often quite complex capabilities
  Cannot usually understand partitions or file systems
First-stage Bootloader (PCs: SysLinux, MIPS: Das Uboot)
  Found on a storage device (e.g. HDD)
  Very small (~512 bytes)
  Often very simple capabilities w.r.t. devices
  Can read partition tables
  Loads second stage (or, on embedded, the OS itself)
Second-stage Bootloader (PCs: SysLinux, MIPS: None)
  Found on a storage device (e.g. HDD)
  Variable size, often large
  Complex capabilities all round (e.g. GRUB/GRUB2)
  Loads & starts the OS
SysLinux – nothing to do with Linux

## Slide 4: Re-cap (3)
OS:
  Kernel
  Drivers (Kernel-mode) e.g. keyboard driver, HDD driver
  Apps (User-mode) e.g. Text editor, command prompt, web browser
Kernel-mode vs User-mode
What are we looking at? Kernel only.
  It’s more than enough to keep us busy!

## Slide 5: This week:
Let’s get some coding done!
A basic, bootable x86 kernel
A basic, bootable MIPS kernel

## Slide 6: What are we going to need?
Toolchain
  Compiler
  For CI20s: USB OTG Boot tool, USB2Serial connectors
Compiler:
  Needs to be a cross-compiler
  Even for x86! Because we need to output ELF not PE
  Unless you’re already on Linux
  But then we’re going to have “fun” with MIPS development…
C or C#? Neither. We’re using ASM for this first bit.

## Slide 7: Where can I get this stuff?
Windows:
  https://github.com/FlingOS/Getting-Started-Tutorials/tree/master/2.%20Booting/Code for sample code + toolchain
Linux/OSX:
  https://github.com/FlingOS/Getting-Started-Tutorials/tree/master/2.%20Booting/Code for sample code
  Install GCC
  Adapt the build script to match your path to GCC
What about MIPS?
  Sourcery CodeBench
  But: We’re a bit stuffed because MentorGraphics started charging money and there’s no trial version of the MIPS compiler
  I’ve not looked into it but this might work: http://community.imgtec.com/developers/mips/tools/codescape-mips-sdk/download-codescape-mips-sdk-essentials/
  Samples in the lectures repository

## Slide 8: What’s in here? PC first.
ISO folder – files which go straight into the ISO file
  Kernel.bin – copied during the build. This is your OS.
  Isolinux-debug.bin – a pre-built, debug version of the main SysLinux bootloader specifically for ISO files
  Ldlinux.c32, libcom32.c32 – pre-built binaries required by SysLinux
  Mboot.c32 – a pre-built plugin to SysLinux that adds support for multiboot
  Syslinux.cfg – the config file used by SysLinux to support multiple OS’es and define the default OS (and more complex stuff if you need it)
Tools folder – the compiler toolchain
  Cygwin/ld.exe – The linker (ld)
  Cygwin/objdump.exe – Used to generate human readable info about binary files
  NASM/nasm.exe – The assembler. Takes x86 NASM Assembly code and generates machine code (stored in ELF format)
  ISO9660Generator.exe (& Mosa….dll) – wrapper tool used to generate the .ISO file
Kernel.asm – Your kernel assembly file!
Kernel.bin – auto-generated during build. Machine code of your OS (output of ld)
Kernel.o – auto-generated during build. Object file, ELF format (output of NASM)
SampleKernel.iso – Your OS! You can use this in a VM.
Linker.ld – The link script. It’s a really simple one.

## Slide 9: What’s in here? MIPS next.
Pretty similar to x86
Main.c – Okay so we have a basic C file
Start.s – Some bootstrap assembly
Linker.lds – A simple link script for targeting CI20

## Slide 10: What about testing it all?
x86/PC:
  Virtual Machines – VMWare or VirtualBox
  Real hardware – USB boot to laptops
MIPS:
  Creator CI20s (boot over USB2Serial)
Can I use a debugger?
  Did you program support into your OS? No? Well, probably not then! 

## Slide 11: That’s lots of information…
So let’s start the workshop and see if we can put it all together!