## Slide 1: Week 3
ASM & Initialisation

## Slide 2: Re-cap
Boot sequence:
  BIOS (ROM, Access devices but not partitions/file systems (FS))
  First stage bootloader (Storage device, Access FS but not devices)
  Second stage bootloader (Storage device + file system, Access all)
Processor features:
  Registers (General Purpose + Specialist + Config + Control)
  FPU
  EPU
  MMU
I/O Ports
Kernel, Drivers and Apps
  Kernel mode vs User mode
  We are looking at?
Basic bootable OS

## Slide 3: Assembly Language
Let’s write some examples!
  Use of x86 general purpose registers
  Some special uses of the GPRs
  Branch operations: Jump, Loop
  Comparison instructions
  Conditional branches
  Accessing flags
  Accessing I/O ports

## Slide 4: Processor Initialisation
Why do we need to do this?
What steps are involved?
  Check for Multiboot
  Switch to Protected Mode
    What is Real Mode?
    What is Protected Mode?
  Setup space for the stack
  Configure a GDT
  Tell the CPU about the GDT
That’s it for now…

## Slide 5: Checking for Multiboot
Signature value in EAX
0x2BAD2B002
Compare values:
  If not there: print out message & halt
  Otherwise: Continue
Load some information (e.g. size of memory areas)
  Multiboot info structure

## Slide 6: Processor Modes
Real Mode
  No process isolation
  No OS control
  No multitasking
  Not originally called Real Mode – named after PM was added
  No access to memory beyond 1MiB (except for some hacks)
  Side note: A20 Gate
Protected Mode
  All the nice things
  Virtual Memory
  Multitasking (see Task State Segment – TSS + GDT)
  Access to full 4GiB (or 16 Exbibyte (EiB) on a 64-bit system…if you have space)
  Side note: Still requires A20
  Many other useful features
So how do we switch?

## Slide 7: Stack
Allocate space in kernel image (/binary)
Tell the CPU where the stack starts

## Slide 8: GDT
Global Descriptor Table
Used for segmented virtual memory
And for multitasking (see TSS)
But nobody uses segmented memory anymore?
So we set up segments to cover the entire address space and all task privileges
And then we give the CPU a pointer to a pointer structure to the GDT
A pointer to a pointer structure? Yes, it’s a bit weird but there’s a good reason: The CPU needs to know the size of the GDT
  Not size: Max offset! So Size-1!
Then we must update the segment registers inc. doing a long-jump

## Slide 9: Your turn…