## Slide 1: Week 4
GDT & Using C

## Slide 2: Thus far…
x86 & MIPS architectures
Boot sequences
Multiboot standard
Processor initialisation

## Slide 3: This week
GDT – final part of processor initialisation
Using C – looking at:
  Compiling & linking in more detail
  How to call a C function from ASM

## Slide 4: GDT
Global Descriptor Table
Implements segmented virtual memory
  Example from video : https://youtu.be/zJFsxYDbDrs?t=9m14s
Why is it necessary?
  Legacy requirement
How?
  Fixed table allocated at compile time
  Cover every (practical) combination of permissions & area
  Point processor at correct table
  Update segment registers

## Slide 5: Compiling
Conversion of text to machine code
Multi-stage process
GCC:
  C to ASM code
  ASM to machine code (referred to as object files at this stage)
  All files still kept separate (.c -> .s -> .o)
Machine code is in ELF format
Addresses are placeholders
(Static) Linker (Ld) will insert the addresses

## Slide 6: Linking
Combines machine code (object files)
Into single file: final binary or libraries
Replaces placeholders with our desired addresses
  Extern & Global keywords
Uses link script to specify how the output should be laid out
  Layout in terms of segments and sections
  Sections exist in the original (ASM) code
  Layout in terms of addresses / ordering
Produces the final machine code (binary file)
Machine code also in ELF format but without placeholders
ELF format also specifies entry point
Bootloader understands and loads ELF as intended

## Slide 7: Typical sections
.text
  Code
.bss
  Uninitialised data
.data
  Initialised data
Other sections/segments exist

## Slide 8: Compiling C
GCC (and ld) command:
  gcc Kernel.o main.c -o Kernel.bin -T linker.ld -nostartfiles –nostdlib
Explanation:
  gcc – Name of the executable (different versions of gcc exist!)
  Kernel.o – The object file produced by NASM (from Kernel.asm)
  main.c – The input c file to compile & link (can specify more)
  -o Kernel.bin – Name of the output file
  -T linker.ld – Name of the link script to use
  -nostartfiles – Prevents renaming of compiled functions (e.g. main to _main)
  -nostdlib – Prevents gcc trying to include the standard libraries

## Slide 9: Calling C from ASM
Name of C function must be declared EXTERN
Just do a “call” to the c function
-nostartfiles means it won’t have been renamed by gcc

## Slide 10: Linking C
GCC calls Ld for us
  With the link script we specified

## Slide 11: Putting it all together
Let’s write colour output code
In C!
And compile & link it!